## Slide 1: Satellite data assimilation applications: Mesoscale (and cloud-resolving)
Milija Zupanski
Cooperative Institute for Research in the Atmosphere
Colorado State University
Fort Collins, Colorado
JCSDA Summer Colloquium
CIRA/Colorado State University, Fort Collins, CO
July 27 – August 7, 2015

## Slide 2: History – assimilation
Yoshi Sasaki (1927-2015)
Calculus of variations
Variational weak and strong constraints
Variational principles are important for data assimilation
from Lewis (2009)

## Slide 3: History - prediction
Ed Lorenz (1917-2008)
Chaotic dynamics (inserts from the 2006 presentation at FSU, Tallahassee)
Data assimilation is closely connected to chaotic/nonlinear dynamics

## Slide 4: Overview
Motivation
Satellite data assimilation and clouds
Challenges
Applications with WRF model

## Slide 5: Motivation: High-impact weather
Thunderstorms
Tornadoes
Rainfall
Hail
Flash floods
GOES-R
  Mississippi tornado (04/2011)
Cloud-resolving (CR) modeling typically implies:
- high dimensionality
- cloud microphysics (bulk, 1-2-moment microphysics)
- parallel processing (MPI, Open MP)
Cloud hydrometeor prediction is in the focus of CR applications

## Slide 6: Motivation: Clouds
Clouds: information to be utilized
  Typically associated with high impact weather
  Can produce extreme rainfall and floods
  Cloud microphysics
  Radiation
GOES-R
  Hurricane Dora (2012) - GOES
  Supercell thunderstorm cloud (2010) - NASA
Improving analysis and prediction of clouds is challenging, but fundamentally important

## Slide 7: Motivation-3: New satellites
GPM
GOES-R
Applications
High-impact weather
Precipitation (water vapor, clouds)
Air pollution (aerosol, SO2, NO2, O3)
NASA Global Precipitation Mission (GPM) satellite
Dual-frequency precipitation radar (DPR)
GPM microwave imager (GMI)
NOAA Geostationary Operational Environmental Satellite(GOES-R)
Advanced Baseline Imager (ABI)
Geostationary Lightning Mapper (GLM)
Korean Environmental Satellite (MP-GEOSAT)
Geostationary Environment spectrometer (GEMS)
ABI + GOCI-2 (ocean color)
Solar Panel
ABI
GOCI-2
Solar Panel
GEMS

## Slide 8
Satellite observations relevant for clouds
Microwave radiances
Infrared radiances
Spaceborne lightning
Spaceborne radars

## Slide 9
Satellite observations relevant for clouds: Microwave radiances
Penetrate clouds, can “see” inside
Related to microphysics
Channel 1: 23.8 GHz
20 May 2013, 12z
Weighting function: Surface
Channel 3: 53.6 GHz
20 May 2013, 12z
Weighting function: 650 hPa
Channel 9: 57.3 GHz
20 May 2013, 12z
Weighting function: 92 hPa

## Slide 10
Satellite observations relevant for clouds: Infrared radiances
Imager cannot penetrate clouds, can “see” cloud top
Potential benefit for improving the location of a storm
Visible (4 km)
30 May 2013, 13:15z
Water vapor (4 km)
30 May 2013, 13:15z
Thermal infrared (4 km)
30 May 2013, 13:15z

## Slide 11
Combined MW and IR observations of clouds
Microwave
Two images of typhoon Zeb (1998) intensifying in the western Pacific. In the microwave image on the left, dark blue marks a developing eye at the center of circulation. This dark blue coloration suggests abundant low-level cloud water in the eye but no deep convection above. The greens and yellows in the spiral bands represent scattering signatures from precipitation-size ice particles above the freezing level. The infrared image on the right shows the cirrus clouds and cumulonimbus that covers most of the storm. It shows a portion of the eye. However, the northern part of the eye is covered by cirrus clouds. Navy Research Lab Monterey, Marine Meteorology Division.
Infrared

## Slide 12
GOES-R Global Lightning Mapper (GLM) – 2016
Location and strength of the storm and its environment
6-hour lightning observations of Hurricane Ike (2008)
Satellite observations relevant for clouds: Lightning mapper

## Slide 13
GPM Dual-frequency Precipitation radar (DPR)
Satellite observations relevant for clouds: Airborne radar
High-resolution cross-section of clouds
Courtesy of JAXA
CloudSat radar: Chicago flooding (April 2013)

## Slide 14: Satellites and clouds
Satellites observational coverage includes polar regions and open oceans
  - temperature, moisture, winds, clouds
  - chemical constituents
  - ocean surface (waves, tides, algae)
Most high impact weather systems are associated with clouds
- Severe weather
- Tropical cyclones
- Extreme precipitation events
Information about clouds can be very important
- cloud properties (microphysics)
Improving analysis and prediction of clouds is challenging, but fundamentally important
However, current operational systems rarely include assimilation of cloud/precipitation-affected radiances

## Slide 15
GOES-R
Re-development of the TS Erin (2007): Distribution of AMSU-B radiance data in the NCEP operational data stream: (a) all observations, (b) accepted observations after cloud clearing. Data are collected during the period 15-18Z, August 18, 2007. Note that almost all observations in the area of the storm got rejected by cloud clearing. (from Zupanski et al. 2011, J. Hydrometeorology)
Valuable information is lost due to cloud clearing
Need to assimilate all-sky satellite radiances
Impact of cloud clearing

## Slide 16: Mesoscale/CR data assimilation application is a magnifying glass for data assimilation deficiencies
Mesoscale and cloud-resolving data assimilation is:
Nonlinear
Microphysical processes are nonlinear
Scattering makes radiative transfer operator nonlinear
Non-differentiable
Radiative transfer with scattering
Ice/liquid water content assimilation
Non-Gaussian
Cloud, moisture, chemistry, aerosol control variables
High-dimensional
Some standard DA techniques have limitations in high dimensional problems
Computing efficiency can be hampered
Multivariate, time-dependent
Balances between variables are not known, or difficult to represented in the forecast error covariance
Highly correlated and complex dynamics

## Slide 17: Global and limited-area CR data assimilation
Global domain:
Number of potentially challenging points is relatively small compared to all model points
This implies a small contribution to the cost function

## Slide 18: Global and limited-area CR data assimilation
Limited area mesoscale-CR domain
Nonlinear points can dominate in the model domain
Large contribution to the cost function
Inadequate treatment of challenging points can only marginally impact global DA, but effectively destroy the limited-area mesoscale and cloud resolving DA
Global domain:
Number of potentially challenging points is relatively small compared to all model points
This implies a small contribution to the cost function
Computational cost considerations?

## Slide 19: How is radiance included in data assimilation?
GOES-R
Additional term in observation cost function
Tb – Brightness temperature (equivalent to radiance)
RT – radiative transfer equation operator
Methodologically is simple adding satellite radiances
Problem comes from:
- high number of observations
- slow calculations of RT
- imperfect calculations of RT (radiance bias correction)

## Slide 20: Forecast error covariance in cloud-resolving satellite data assimilation
Only dynamical auto-correlations are relatively well known
Correlations among microphysical variables are generally unknown
Even less known are the cross-correlations between dynamical and microphysical variables
Correlations between dynamical variables
Correlations between microphysical variables
Cross-correlations between dynamical and microphysical variables
Complex inter-variable correlations

## Slide 21: Single observation of cloud snow at 650 hPa: ensemble DA response in vertical
Vertical analysis increments for (a) snow, and (b) rain.
(a) Snow at 34N (Psnow,snow)
(b) Rain at 34N (Prain,snow)
Difficult to model rain-snow correlation:
non-centered response and time-dependence
X

## Slide 22: High dimensionality implications on cloud-resolving satellite data assimilation
Computational and scientific challenge
Complex cloud-resolving processes would most benefit from ensemble-based error covariance
Flow-dependent error covariance requires ensemble forecasts
Given the high computational cost of cloud-resolving model, only a small number of ensemble forecasts is feasible
Small number of ensembles implies poorly estimated forecast error covariance

## Slide 23: Typical computational approximation (model-space-VAR)
Neglect the impact of observations in matrix inversion
Use iterative minimization
Simplify matrix formulation in order to accomplish matrix inversion

## Slide 24: Typical computational approximation (ENS)
Define ensemble-based forecast error covariance in order to invert the matrix
Reduce the number of degrees of freedom in order to accomplish matrix inversion

## Slide 25: Error covariance localization and satellite radiance assimilation
Error covariance localization is used in ensemble DA to increase the number of degrees of freedom
+
Original error covariance
Localizing function
Final localized error covariance
Localization implies local impact of observations. However, satellite radiances are vertically integrated observations!
Meteosat Second Generation
Need to pay special attention to vertical localization in Ensemble and Hybrid DA

## Slide 26: Radiance bias correction
Biases in radiance innovations [y-h(x)] are mainly caused by systematic errors in prediction model inputs to radiative transfer model
- biased surface conditions (e.g., skin temperature)
- excessive snow or ice content
- excessive precipitation near boundaries
Typical approach is to use linear regression
WRF skin temperature
Input to RTM 2009-09-19-18z
p = predictor
= regression parameter

## Slide 27: Maximum Likelihood Ensemble Filter (MLEF): Forecast
In KF, the forecast error column is a forecast of the analysis error column
Since spans the analysis uncertainty subspace, one can say that uncertainty is transported in time by a (linear) model M
Each uncertainty column vector is a member of an“ensemble” (i.e. span)
Transport uncertainty in time by a nonlinear model m (one span vector at a time)
Generalize KF to include nonlinear forecast model:

## Slide 28: Maximum Likelihood Ensemble Filter (MLEF): Analysis
In standard KF, the analysis is obtained by minimizing a
quadratic cost function (i.e. with linear observation operators)
Control theory viewpoint:
Generalize KF to include nonlinear observation operators:
Minimize nonlinear (i.e. non-quadratic) cost function
Use best applicable minimization method
Build data assimilation around minimization

## Slide 29
MLEF overview
“Ensembles” are not considered random
- Information processing (Shannon) rather than a statistical update
- Side product is the observation information content (entropy change)
Full-rank or Reduced-rank
- Computational considerations (low/high-dimensional modeling systems)
Nonlinear minimization:
- Generalized gradient-based methods (Zupanski et al. 2008)
- Non-smooth methods (Steward et al. 2012)
3D, 4D approach:
- 3D or 4D control variable (and error covariance)
Additional details:
- No covariance inflation
- Use both enforced and dynamical covariance localization
- Control variable includes initial conditions and/or empirical parameters
Notes: Outline slide

## Slide 30: Precipitation: NASA Global Precipitation Mission - GPM: Downscaling satellite precipitation information using ensemble data assimilation
Assimilate precipitation-affected microwave satellite radiances
AMSR-E, TMI, AMSU-A,B, MHS
Provide improved precipitation information for hydrology models
Cloud-scale data assimilation with NASA WRF model (27-9-3-1 km)
Sara Zhang et al. (2012), Mon. Wea. Rev.
Surface precipitation short-term forecasts verification
(accumulated during 15-22 Sep 2009 in the southeast US flood region)
Ground-based Verification
(NOAA Stage IV data)
3DVAR, no AMSR-E,TMI
(WRF-GSI)
EDAS, with AMSR-E, TMI
(WRF-EDAS)

## Slide 31: Assimilation of GPM Microwave Imager (GMI) all-sky satellite radiances
NASA Unified WRF (NU-WRF) at 9km/3km
32 ensembles, 3-hour assimilation interval
Control variable includes dynamic and cloud variables
(Valid 15 May 2014 at 0000 UTC)
Positive impact of GMI radiance assimilation on precipitation and near-surface wind.
The accumulated precipitation forecast (0-6 h) is improved by 23% in RMSE verified using ground validation observations.
GMI 89GHz
DPR Ku
DPR Ka
Hydrometeor analysis increments
Guess GMI radiance

## Slide 32: Lightning data assimilation
Lightning observation impacts the analyses of specific humidity, temperature and horizontal winds
Lightning observation operator is a regression:
Single observation experiment using h1 operator
Q at 850 hPa
T at 850 hPa
(u,v) at 850 hPa
Karina Apodaca (karina.apodaca@colostate.edu)

## Slide 33
Chart: 
| 3.92124E-8 | 1.09135E-7 | 3.20489E-7 | 9.09465E-7 | 2.47334E-6 | 7.14547E-6 | 2.11518E-5 | 5.79068E-5 | 0.000141232 | 0.000282077 | 0.000630117 | 0.00139574 | 0.00218932 | 0.00373509 | 0.00556658 | 0.00420806 | 0.00322917 | 0.00240605 | 0.00170613 | 0.00113905 | 0.000745639 | 0.000486467 | 0.000320249 | 0.000206797 | 0.000117259 | 5.28029E-5 | 1.95118E-5 | 7.30824E-6 | 2.93324E-6 | 1.12142E-6 | 4.06936E-7 | 1.41854E-7 | 4.84671E-8 | 1.97114E-8
GSI+LIGHT | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
GSI | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
Difference | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
Pressure (hPa)
Graupel Mixing Ratio (g/kg)
Impact of lightning DA on cloud hydrometeors using h2
QICE (g kg-1)
Pressure (hPa)
Chart: 
| 2.96922E-9 | 9.25981E-9 | 3.01697E-8 | 9.54322E-8 | 2.89691E-7 | 8.37713E-7 | 2.28909E-6 | 5.86416E-6 | 1.43717E-5 | 3.39767E-5 | 9.91688E-5 | 0.000382291 | 0.00141617 | 0.00235773 | 0.00341067 | 0.00441635 | 0.00543158 | 0.00615255 | 0.00623473 | 0.0061947 | 0.00580728 | 0.00540123 | 0.00437039 | 0.00288557 | 0.00153025 | 0.000777039 | 0.00039723 | 0.0001913 | 8.89019E-5 | 2.15856E-5 | 1.52332E-6 | 4.54387E-7 | 1.62827E-7 | 6.96392E-8
GSI+LIGHT | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
GSI | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
Difference | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
Cloud Ice Mixing Ratio (g/kg)
Karina Apodaca (karina.apodaca@colostate.edu)
Chart: 
| 2.05017E-8 | 6.29369E-8 | 2.01754E-7 | 6.257E-7 | 1.85319E-6 | 5.19266E-6 | 1.36129E-5 | 3.40696E-5 | 8.86006E-5 | 0.000235088 | 0.000653801 | 0.00218445 | 0.00410925 | 0.00535675 | 0.0084036 | 0.00847968 | 0.00837767 | 0.00753136 | 0.00655212 | 0.00544719 | 0.00415464 | 0.00287062 | 0.00180924 | 0.00108726 | 0.000614113 | 0.000293593 | 9.49225E-5 | 2.13743E-5 | 7.15107E-6 | 2.58295E-6 | 8.74899E-7 | 2.87167E-7 | 9.23905E-8 | 3.53982E-8
GSI+LIGHT | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
GSI | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
Difference | 1009.63 | 1001.44 | 990.37 | 976.406 | 959.072 | 937.404 | 911.404 | 879.473 | 843.538 | 807.603 | 771.669 | 721.475 | 659.302 | 601.557 | 547.976 | 498.31 | 452.322 | 409.788 | 370.494 | 334.238 | 300.828 | 270.082 | 241.828 | 215.904 | 192.154 | 170.434 | 150.605 | 132.536 | 116.105 | 101.195 | 87.6972 | 75.5069 | 64.5264 | 54.6634
Cloud Snow Mixing Ratio (g/kg)
Pressure (hPa)

## Slide 34: Impact of lightning DA on 3-hour forecast of lightning
LIGHT
Observed
GOES-15 Infrared
CTL
Improved representation of storm structure through more accurate location and intensity of lightning activity
Tropical storm Ivo (2013)
CTL: NOAA/NCEP data assimilation algorithm (no lightning)
(2) LIGHT: same as CTL, but with assimilation of lightning (h2)
Karina Apodaca (karina.apodaca@colostate.edu)

## Slide 35
Summary and Future
Assimilation of cloud/precipitation affected radiances is important for mesoscale and cloud-resolving modeling systems
- Preliminary results for severe weather, precipitation applications
- Benefit from unique geographical coverage over open oceans, polar regions
Challenges of cloud/precipitation affected radiance assimilation
- nonlinear/non-differentiable RT operator
- radiance bias correction
- correlated observation errors
- non-Gaussian observation errors
- land emissivity
Assimilation of lightning from satellites (e.g., GOES-R)
- lightning flash rate can impact the storm and its environment
Assimilation of atmospheric chemistry/aerosol information from radiances
- air pollution/quality, dust storms
Notes: Outline slide

## Slide 36
Thank you!
References:
Apodaca, K., M. Zupanski, M. DeMaria, J. Knaff, and L. Grasso, 2013: Evaluating the potential impact of assimilating satellite lightning data utilizing hybrid (variational-ensemble) methods. Submitted to J. Appl. Met. Clim.
Chambon, P., S. Q. Zhang, A. Y. Hou, M. Zupanski, and S. Cheung, 2013: Assessing the impact of pre-GPM constellation microwave precipitation radiance data in the Goddard WRF ensemble data assimilation system. Quart. J. Roy. Meteorol. Soc., DOI:10.1002/qj.2215.
Steward, J. L., I. M. Navon, M. Zupanski, and N. Karmitsa, 2012: Impact of Non-Smooth Observation Operators on Variational and Sequential Data Assimilation for a Limited-Area Shallow-Water Equation Model. Quart. J. Roy. Meteorol. Soc., 138, 323-339.
Zhang, M., M. Zupanski, M.-J. Kim, and J. Knaff, 2013: Assimilating AMSU-A Radiances in TC Core Area with NOAA Operational HWRF (2011) and a Hybrid Data Assimilation System: Danielle (2010). Mon. Wea. Rev., doi:10.1175/MWR-D- 12-00340.1, in press.
Zhang, S. Q., M. Zupanski, A. Y. Hou, X. Lin, and S. H. Cheung, 2013: Assimilation of precipitation-affected radiances in a cloud-resolving WRF ensemble data assimilation system. Mon. Wea. Rev., 141, 754-772.
Zupanski D., M. Zupanski, L. D. Grasso, R. Brummer, I. Jankov, D. Lindsey and M. Sengupta, and M. DeMaria, 2011: Assimilating synthetic GOES-R radiances in cloudy conditions using an ensemble-based method. Int. J. Remote Sensing, 32, 9637-9659.
Zupanski, D., S. Q. Zhang, M. Zupanski, A. Y. Hou, and S. H. Cheung, 2011: A prototype WRF-based ensemble data assimilation system for downscaling satellite precipitation observations. J. Hydromet., 12, 118-134.
Zupanski, M., 2005: Maximum Likelihood Ensemble Filter: Theoretical Aspects. Mon. Wea. Rev., 133, 1710–1726.
Zupanski, M., I. M. Navon, and D. Zupanski 2008: The maximum likelihood ensemble filter as a non-differentiable minimization algorithm. Q. J. Roy. Meteor. Soc. 134, 1039-1050.
Zupanski M., 2013: All-sky satellite radiance data assimilation: Methodology and Challenges. Data Assimilation for Atmospheric, Oceanic, and Hydrologic Applications, S.-K. Park and L. Xu, Eds, Springer Heidelberg New York Dordrecht London, pp. 465-488.
[http://ensembleda.cira.colostate.edu]
Notes: Outline slide