## Slide 1: Basics of Satellite Observations
Will McCarty
Global Modeling and Assimilation Office NASA Goddard Space Flight Center
2015 JCSDA Summer Colloquium
28 July 2015

## Slide 2: Acknowledgments
First, parts of these two talks (Basics of Satellite Observations and Infrared Remote Sensing) are drawn from the previous talks of Chris Barnet. He was kind enough to give me his talks and full permission to take from them
Second, a large portion of the figures in this talk were found via google. I didn’t do a good job of giving credit where due, but I don’t deserve credit on many of them

## Slide 3: My Background
B. S. Meteorology
  Valparaiso University (2003)
M.S., Ph. D. Atmospheric Science
  Univ. of Alabama in Huntsville (2005, 2008)
Global Modeling and Assimilation Office
  NASA Goddard Space Flight Center
  Since January 2009
Of Note:
  Summer 2006 (I think) – Spent summer at WWB working w/ John LeMarshall (then-director of JCSDA)
  Summer 2007 – Student at the first JCSDA Summer Colloquium

## Slide 4: Satellite Basics
What I won’t cover, but can at least address offline if you’re interested:
  Anything that looks upwards
    Links between ground-based and satellite remote sensing
    Links between earth science and space science
This talk will present a number of characteristics of satellite observations, hopefully introducing key terminology

## Slide 5: Launch Vehicle/Satellite

## Slide 6: Launch Vehicle/Satellite

## Slide 7: Satellite/Instruments
7
Delta-II-7920
Vandenburg AFB
VIIRS
ATMS
CERES
OMPS (electronics)
OMPS Nadir, limb
CrIS
X-band DB Antenna
X-band 300 Mb/s Antenna
S-band C+T Antenna
Cubesats

## Slide 8: Orbit Characteristics
Satellites orbit as the result of the gravitational force that is equivalent to the net centripetal force
Let’s assume a circular orbit…

## Slide 9: Orbit Characteristics
Variable | Value | Description
 | constant | Satellite height above surface
 | 6,378,137.0 m | Earth Radius at equator The earth is not a perfect sphere but an oblate spheroid ()
 | 5.972 x 1024 kg | Mass of the Earth
 | unknown | Satellite Velocity
G |  | Gravitational constant
Variable | Value | Description
 | constant | Satellite height above surface
 | 6,378,137.0 m | 
 | 5.972 x 1024 kg | Mass of the Earth
 | unknown | Satellite Velocity
G |  | Gravitational constant

## Slide 10: Orbit Characteristics
All that matters for your orbit is that put it at the right height at the right velocity!

## Slide 11: Orbital Characteristics
Now you can play games to determine different orbits, and these can be used to determine idealized sampling strategies
We will now walk through a few typical (and atypical) types of orbits in the earth sciences
  Sun-synchronous
  Geosynchronous (or geostationary)
  Molniya
  Low inclination, low-earth orbits

## Slide 12: Orbital Characteristics
Quick definitions:
Orbit Inclination
  The angle of the orbit relative to the equator
Orbit Period
  The time it takes to complete a full orbit
Orbit Node
  The ascending node is when the satellite travels from south to north, and the descending node is from north to south

## Slide 13: Sun-Synchronous Orbits
  Low-earth orbit (~800 km)
  High Inclination (polar orbit)
  Orbit period is set based a fractional rotation of the earth underneath it
    The satellite overpasses the equator at the same local time on its ascending node (e.g. noon at that point)
    e.g. 10 orbits per day? Then the period must be 144 minutes
      10 orbits * 144 min = 24 hr * 60 min
  Orbital plane is consistent in position to the sun
  Allows for consistent global sampling daily

## Slide 14: Geosynchronous (Geostationary) Orbit
  High Earth Orbit (~35000 km)
  0° Inclination (orbits over equator)
  Angular velocity of satellite is equal to the angular velocity of Earth
    The relative velocity of the satellite to the earth’s surface is zero
    Therefore, the orbital period is 1 day, just like the earth
  Allows for good local temporal resolution below satellite
    multiple satellites are required for global coverage
    Also, weak for viewing poles because of high viewing angles

## Slide 15: Molnyia Orbit
  Highly elliptical
  Provides long dwell over the north (or south if flipped) polar regions
  Named after a series of Soviet military communication satellites in the 1960s
  Has been proposed that a small constellation (~3 satellites) could provide geostationary temporal resolution for the poles

## Slide 16: Molnyia Orbit

## Slide 17: Low-Inclination Orbits
  Generally circular orbits at with inclination set to study a specific question
    Tropical Rainfall Measurement Mission (incl = 35°)
    Global Precipitation Mission (incl = 65°)
    RapidScat Instrument
      Payload on International Space Station (incl. = 51.6°)
  Not sun-synchronous, so diurnal information can be obtained
  The relative position to the sun can differ, resulting in complicated satellite maneuvers in space as a result more complicated power management
TRMM
ISS-RapidScat

## Slide 18: Other Orbits
These are a sampling of the key meteorological orbits, but there are others of note
  GPS orbits (circular in medium earth orbit @ ~ 2000 km)
  Space sciences use all sorts of different orbits

## Slide 19: Atmospheric Radiation
At their core, satellite instruments measure atmospheric radiation
Types of radiation are defined in spectral space by:
  Frequency (f) – the number of waves of radiation per second (Hz)
  Wavelength (λ) – the length of a single wave of radiation (m)
  Wavenumber () – one over the wavelength (1/m)
   = 1/ λ ; λf = c

## Slide 20: Atmospheric Radiation
Basic Categories in our field:
  Ultraviolet (λ < 400 nm)
  Visible (400 nm < λ < 700 nm)
  Infrared (0.7 μm < λ < 1 mm)
  Microwave (λ > 1 mm)
For this talk, I’m going to keep it that simple.

## Slide 21: Very Simple Radiative Transfer
Something emits a photon (or light/radiation particle) at a given wavelength as a function of its temperature
When a photon interacts with a medium (gas, a surface, anything), it is either:
  Transmitted – passes through with no interaction
  Reflected – bounces off the medium
  Absorbed – the energy of the photon is incorporated into the internal energy of the medium
 | Temperature | Peak Wavelength | Type of Radiation
Sun | 6000 K | 500 nm | Visible Light
Earth | 290 K | 10 μm | Thermal Infrared

## Slide 22: Very Simple Radiative Transfer
The efficiency of these three processes are known as transmissivity (t), reflectivity (ρ), and absorptivity (α), and their sum is equal to 1.0
T = 1.0
t = 1.0
ρ = 1.0
α = 1.0
t = ρ = α = 0.333
=

## Slide 23: Very Simple Radiative Transfer
When considering the atmosphere, where there are many different molecules and particles interacting, radiation (many photons) can be scattered
When radiation is scattered back to the source (satellite), that is called backscatter

## Slide 24: Instrument Characteristics
Active vs. Passive
  Active Instrument: Measures the return reflected by an observed feature from an actively emitted (man-made) source
    e.g. Radar, Lidar
  Passive Instruments: Measures the radiation emitted or reflected from the observed feature from a natural source (generally Sun and Earth)
    e.g. Radiometer

## Slide 25: Active Instruments
In atmospheric sciences, active instruments generally break down into three sources
  Radar
  Lidar
  GPS-Centric

## Slide 26: Active Instruments
Radar: a microwave pulse is emitted from the satellite and the backscatter is measured
  Some spaceborne radars are cloud- and precipitation profiling
  Scatterometry uses a radar to measure surface roughness, which is related to wind speed.
    Many measurements from different angles can be used to determine a surface wind vector
  Examples:
    CloudSat Cloud Profiling Radar
    TRMM Precipitation Radar
    GPM Dual-Frequency Precip Radar
    RapidScat Scatterometer

## Slide 27: Active Instruments
Lidar: An ultraviolet/visible/near-infrared pulse of light is emitted and the backscatter is measured
  Smaller wavelengths means sensitivity to smaller particles
  Often used for thin cloud and aerosol studies
Examples:
  CALIPSO Cloud-Aerosol Lidar with Orthogonal Polarization (CALIOP)
  ISS Cloud Aerosol Transport System (CATS)
  ICESat Geoscience Laser Altimeter System (GLAS)
Lidar is more sensitive to small aerosols. Here dispersants from the BP Deepwater Horizon Oil Spill are seen
Note the lidar data is subject to attenuation by clouds, while radar can penetrate through

## Slide 28: Active Instruments
GPS: the characteristics of a GPS signal emitted from another satellite is measured and used to determine geophysical information
  GPS Radio Occultation
    Vertical profiles of refractivity, which is related to temperature and moisture
  GPS Surface Wind Speed
    Surface roughness is determined by measuring GPS signals reflected off the ocean surface
  Lidia will talk more on this tomorrow

## Slide 29: Passive Instruments
Passive instruments generally measure either:
  Solar radiation reflected by the earth
  Terrestrial radiation emitted by the Earth System
    Surface and atmosphere
Passive instruments are generally classified into two types:
  Imager
    Instruments that focus on horizontal resolution
  Sounder
    Instruments that focus on vertical resolution
Fundamental to all satellite instruments is the concept of resolution

## Slide 30: Fundemental Measurements
Radiance
  In wavenumber space:
  or, energy per second (mW) per unit area per unit of solid angle viewing (steradian) per wavenumber (cm-1)
Irradiance
  Earth Radiation Budget Experiment (ERBE), Clouds and the Earth's Radiant Energy System (CERES)
  Generally,
  Or Energy per second (J/s, or W) per unit area
Irradiance is simply radiance integrated over viewing area and wavenumber

## Slide 31: Satellite Resolution
At a basic level, satellites are measuring the number of photons hitting a detector over a given time
The detector will have some quantifiable accuracy of how many photons it can detect over an integration period
Detector accuracy translates to a trade-off study of different types of resolution:
  Spatial
  Spectral
  Temporal
  Radiometric

## Slide 32: Satellite Resolution
Spatial Resolution
  Observations are made over a viewing cone (IFOV)
  Width of this cone affects the amount of photons that reach the detector
Spectral Resolution
  Satellites measure over a spectral response function
    For some instruments this may be small (fractions of a cm-1) and others large (many microns)
  Spectral resolution is analogous to vertical resolution
    Figuratively in land surface remote sensing
    Literally in the case of temperature and moisture remote sensing

## Slide 33: Satellite Resolution
Temporal Resolution
  Amount of time between observations of the same earth spot
  Affects observation accuracy because better temporal resolution requires higher orbits
    Sun-Synchronous ~800 km (2x / day), Geostationary ~35000 km (4x / hour)
    Inverse square law
Radiometric Resolution
  The amount of pieces of data that can be discerned
  Bits of information!
2-bit
8-bit

## Slide 34: Satellite Design
The ultimate goal of all of these trade offs are to come up with a platform that is technically feasible but scientifically useful
  The bridge between satellite engineers and scientists is often a balance of what can be measured and how it is measured
  In terms of harsh stereotypes:
    Engineers don’t care about the use of the data, only on how the system can be designed to get the optimal measurement within the limits of technology
    Scientists don’t care why the measurements are limited, they just want all the data possible and typically more data and better data than is feasible

## Slide 35: Satellite Design
The ultimate goal of all of these trade offs are to come up with a platform that is technically feasible but scientifically useful
  The bridge between satellite engineers and scientists is often a balance of what can be measured and how it is measured
  In terms of harsh stereotypes:
    Engineers don’t care about the use of the data, only on how the system can be designed to get the optimal measurement within the limits of technology
    Scientists don’t care why the measurements are limited, they just want all the data possible and typically more data and better data than is feasible
    Program managers get the fun of balancing all this within a cost cap

## Slide 36: Observations as a Function of Time
Observations assimilated per 6-hr cycle
The vast majority of observations over the modern era (1979-onward) are of satellite origin
  This excludes SSMIS. Using SSMIS, the total eclipses 5 million

## Slide 37: Satellites in the Global Observation System
Animation

## Slide 38: The Variational Approach for Satellite Data
  y – H(x) = y – (H(xb) + Hδx)
H(x) transforms the background/guess state to observation space
  If in the same space, as simple as an interpolation
  If in different space, H can be radiative transfer (radiances), a projection of the wind…
  anything to relate analysis space to observation space (well, that can be linearized to H)

## Slide 39: Satellite Data Assimilation
A fundamental part of satellite data assimilation is an understanding of both the assimilation process and the observations
  And all the assumptions underlying
The use of retrieved quantities adds another set of assumptions
  Some retrievals will be more compatible with data assimilation than others
The modern observing system is debatably saturated
  It is difficult to gain quantifiable impact by adding new instruments via existing methodologies